## Slide 1
QUADRUPED ROBOT DEVELOPMENT
━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━
Certification-Based Industrial Training
WTL & MeitY Project | Group-E
Department of Electronics & Communication Engineering
Cooch Behar Government Engineering College | 2026
Guided by: Dr. Palash Das (ECE) | Mrs. Susmita Banik Barik (Project Eng., WTL) | Mr. Arijit Bhunia | Mr. Bhaskar Mondal

## Slide 2
Team Members — Group E
Department of ECE, CGEC | WTL & MeitY Project | 2026
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
2/21
#
Name
Roll No.
Reg. ID
1
Sarupya Guha
34900323046
FS08A0198
2
Sohan Ghosh
34900323050
FS08A0202
3
Sayan Sarkar
34900323048
FS08A0157
4
Debanjan Chakraborty
34900323015
FS08A0154
5
Joydip Das
34900323020
FS08A0220
6
Aushi Sarkar
34900323011
FS08A0288
7
Anupam Dutta
34900323003
FS08A0206
8
Bikkram Das
34900323012
FS08A0528
9
Biraj Sarkar
34900323013
FS08A0239
GUIDED BY
Dr. Palash Das
ECE
Mrs. Susmita
Banik Barik
Proj. Eng., WTL
Mr. Arijit Bhunia
Proj. Co-ord.
Mr. Bhaskar
Mondal
Faculty, WTL
10
Soumyajit Pandit
34900323052
FS08A0189

## Slide 3
Project Objective
What are we building and why?
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
3/21
▶
Design, fabricate & program a fully functional 8-DOF Quadruped Robot
▶
Use affordable, open-source components and tools (ESP32 + FreeCAD + FDM printing)
▶
Core hardware: ESP32 microcontroller | PCA9685 16-ch servo driver | 8 × SG90S servos
▶
Chassis designed in FreeCAD — fabricated with FDM 3D printing (PLA+ & ABS)
▶
Hands-on experience across: Electronics • Mechanical Design • Additive Manufacturing
▶
End goal: Robot capable of standing stably and executing a walking gait
▶
Future roadmap: Sensor integration → Autonomous navigation
▶
Aligned with GoI skills development initiative under WTL & MeitY programme

## Slide 4
Introduction — What is a Quadruped Robot?
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
4/21
▶
A legged mobile robot that moves on four limbs — mimicking dogs, horses, insects
▶
Unlike wheeled robots, quadrupeds navigate uneven terrain, climb stairs, step over obstacles
▶
Each leg has 2+ joints providing degrees of freedom for stable gait generation
▶
This robot: Hip joint + Knee joint per leg → 8 DOF for locomotion
▶
Notable examples: Boston Dynamics Spot • Unitree Go1 • University research platforms
8 DOF
Locomotion (4 hips + 4 knees)
Static Head
Head is stationary
8 Total
SG90S Servos
3 Domains
Electronics Mechanical 3D Printing

## Slide 5
Real-World Applications of Quadruped Robots
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
5/21
🔍 Search & Rescue
Navigates rubble, collapsed structures and disaster zones where wheels cannot go
⚙ Rough Terrain
Pipeline inspection, mining surveys, and remote area monitoring
🎖 Military / Defence
Cargo carrying, reconnaissance missions, and hazardous environment scouting
🏥 Medical / Rehab
Companion and assistive robots for elderly care and rehabilitation
🔬 Research Platform
Studying locomotion algorithms, control theory, and AI-based navigation
🏭 Industrial
Automated factory floor inspection and infrastructure monitoring

## Slide 6
Why ESP32? & Why 3D Printing?
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
6/21
ESP32 — Central Controller
▶
Dual-core 240 MHz processor — powerful yet low-cost
▶
Built-in Wi-Fi & Bluetooth for wireless control
▶
Supports I2C and SPI for peripheral communication
▶
Well-supported Arduino IDE ecosystem
▶
ESP32Servo library — direct servo control via PWM
▶
Wireless capability → OTA updates, remote teleoperation
3D Printing — Chassis Fabrication
▶
Rapid iteration on part dimensions without tooling cost
▶
Customised mounting positions for every component
▶
Fabricate geometrically complex parts cheaply
▶
PLA+ → structural rigidity for Core Body & Head Box
▶
ABS → flexibility & impact resistance for leg links
▶
Entire robot chassis printed in the CGEC 3D Printing Lab

## Slide 7
Development Roadmap — 9-Phase Journey
From component verification to autonomous navigation
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
7/21
Phase 1
Servo & MCU Test
Complete
›
Phase 2
CAD Design
Complete
›
Phase 3
3D Printing
Complete
›
Phase 4
Assembly
Complete
›
Phase 5
Standing Pose
Complete
›
Phase 6
Walking Gait
In Progress
›
Phase 7
Turning Gait
Planned
›
Phase 8
Sensor Integration
Future
›
Phase 9
Autonomous Nav.
Future
Complete
In Progress / Planned
Future Roadmap
📌 This report covers Phases 1–5 in detail. Phases 6–9 form the future roadmap.

## Slide 8
Electronics Architecture
4-Layer electronics stack
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
8/21
Layer 1 — Central Controller
ESP32 Dev Board (I2C Master, Dual-core 240 MHz)
▼
Layer 2 — Servo Driver
PCA9685 16-Channel PWM Driver (I2C Slave @ 0x40)
▼
Layer 3 — Actuators
8× SG90S Metal Gear Micro Servos (4 Hip + 4 Knee)
▼
Layer 4 — Power Supply
External 5V Supply → PCA9685 V+ Servo Rail
ESP32 → PCA9685 Wiring
ESP32 Pin
PCA9685 Pin
3.3V
VCC
GND
GND
GPIO21
SDA
GPIO22
SCL
⚠ PCA9685 V+ rail MUST have an external 5V supply (separate from VCC)

## Slide 9
Servo Channel Mapping
PCA9685 CH0–CH7 → 8 SG90S servos
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
9/21
CH0
Front Left Hip
Type: Hip
CH1
Front Left Knee
Type: Knee
CH2
Front Right Hip
Type: Hip
CH3
Front Right Knee
Type: Knee
CH4
Rear Left Hip
Type: Hip
CH5
Rear Left Knee
Type: Knee
CH6
Rear Right Hip
Type: Hip
CH7
Rear Right Knee
Type: Knee
Hip Servo
Knee Servo
Head Servo

## Slide 10
Critical Discovery — Servo Power Rail Issue
Real-world debugging experience during Phase 1
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
10/21
⚠ SYMPTOM
All 8 servos were completely unresponsive when controlled via PCA9685
🔍 I2C DIAGNOSIS
I2C scanner confirmed PCA9685 at address 0x40 — ESP32, I2C bus, and chip all functioning correctly
🔎 ROOT CAUSE
V+ rail measured only 0.10 V (expected 4.8–5.2 V) — servo power rail NOT connected to external 5V supply
✅ RESOLUTION
Connected 5V directly to PCA9685 V+ terminal → Servos responded immediately. V+ measured 4.92–5.05 V
📖 LESSON
Always verify servo rail voltage FIRST before suspecting firmware or I2C communication issues

## Slide 11
Mechanical Architecture & Component Dimensions
FreeCAD-designed chassis — all parts 3D printed
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
11/21
Structural Overview
▶
Two main assemblies: Head Box (electronics enclosure) + Core Body (central chassis)
▶
Head Box — houses ESP32, PCA9685, power switch + future sensor mount provision
▶
Core Body — mounts all 4 hip servos (4 total on chassis)
▶
Each leg: Upper Leg (hip-driven) + Lower Leg (knee-driven) → 2 links per leg
Component Dimensions
Component
Dimensions (mm)
Notes
Core Body
110 × 85 × 4
4 hip mounts
Head Box
85 × 65 × 45
Wall 2.5 mm — ESP32, PCA9685
Upper Leg ×4
45 × 10 × 5
PLA+ — hip servo driven
Lower Leg ×4
55 × 10 × 5
PLA+ — knee servo driven

## Slide 12
FreeCAD Design Workflow
Part Design workbench — parametric modelling
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
12/21
1
Core Body
Base 110×85×4 mm plate with 4 symmetric hip servo pockets and central head servo mount
2
3
Hip
Four symmetric press-fit pockets at FL, FR, RL, RR corners
4
Upper Leg
45 mm PLA link with servo horn connection hole at proximal end
4
Lower Leg
55 mm PLA link with foot pad boss at distal (terminal) end
5
Head Box
Enclosure designed around ESP32 and PCA9685 PCB footprints (85×65×45 mm)
6
Assembly
All bodies assembled in FreeCAD Assembly with correct spacing and constraints
Hip Servo Mounts
Four symmetric press-fit pockets at FL, FR, RL, RR corners

## Slide 13
3D Printing Process — FDM Technology
CAD → STL → G-code → Print
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
13/21
Fused Deposition Modelling (FDM): thermoplastic filament melted & deposited layer-by-layer | Workflow: CAD Model → STL Export → Slicer (G-code) → 3D Printer
Material Selection
ABS
Core Body, Head Box
High stiffness, low warping, easy to print
PLA
Upper Leg, Lower Leg (×4 each)
Toughness & flexibility for repeated bending/impact loads
Slicer Settings
Parameter
Value
Layer Height
0.2 mm
Infill Density
40%
Perimeter Walls
4
Nozzle Diameter
0.4 mm
Print Speed
50 mm/s
Support
As required

## Slide 14
3D Printing in the Lab
Fabrication of quadruped robot components at CGEC 3D Printing Lab
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
14/21
3D Printer (FDM) in the CGEC Lab during fabrication of the Core Body and Head Box using ABS.
Fabricated leg components (Upper and Lower leg segments) printed in magenta PLA for high layer adhesion and impact strength.

## Slide 15
Products Made — 3D Printed Parts
19 total printed components
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
15/21
Part
Material
Dimensions
Qty
Description
Core Body
ABS
110×85×4 mm
1
Central chassis; 4 hip mounts; 4mm thickness for bending rigidity
Head Box
ABS
85×65×45 mm
1
Electronics enclosure for ESP32, PCA9685 & power switch; 2.5mm walls; future sensor provision
Upper Leg
PLA
45×10×5 mm
4
Hip-servo driven link; servo horn attachment hole at proximal end
Lower Leg
PLA
55×10×5 mm
4
Knee-servo driven link; foot pad boss at distal terminal end

## Slide 16
Arduino Programming
Arduino IDE + ESP32 board support package
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
16/21
Development Environment & Libraries
ESP32Servo
Direct servo control via GPIO PWM
Wire
I2C communication for PCA9685
Adafruit_PWMServoDriver
High-level PCA9685 servo control
Code Listings
Listing 1
Servo Test Code: Direct GPIO18 sweep — 0° → 90° → 180° per servo
Listing 2
PCA9685 I2C Scanner: Scans I2C bus, confirms address 0x40
Listing 3
I2C Scan Output: Expected serial monitor: 'I2C device found at 0x40'
Listing 4
PCA9685 Servo Control: All-channel sweep through Adafruit PWM library
// Servo Test Code — ESP32 direct GPIO18
#include <ESP32Servo.h>
Servo myServo;
void setup() {
myServo.attach(18); // GPIO18
}
void loop() {
myServo.write(0); delay(1000);
myServo.write(90); delay(1000);
myServo.write(180); delay(1000);
}

## Slide 17
Results & Testing
I2C verification · Power rail · All-servo sweep
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
17/21
I2C Communication Verification
PCA9685 confirmed at address 0x40 via I2C scanner
Full chain validated: ESP32 → GPIO21/22 → SDA/SCL → PCA9685
Power Rail Diagnosis & Resolution
Before fix: V+ = 0.10 V (expected 4.8–5.2 V)
After fix: V+ = 4.92–5.05 V → All servos responded immediately
Individual Servo Test Results (All 8 Passed)
#
Function
0°
180°
1
Front Left Hip (CH0)
✓ Pass
✓ Pass
2
Front Left Knee (CH1)
✓ Pass
✓ Pass
3
Front Right Hip (CH2)
✓ Pass
✓ Pass
4
Front Right Knee (CH3)
✓ Pass
✓ Pass
5
Rear Left Hip (CH4)
✓ Pass
✓ Pass
6
Rear Left Knee (CH5)
✓ Pass
✓ Pass
7
Rear Right Hip (CH6)
✓ Pass
✓ Pass
8
Rear Right Knee (CH7)
✓ Pass
✓ Pass

## Slide 18
Development Phase Status
Current progress across all 9 phases
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
18/21
1
Component Verification
Complete
2
CAD Design in FreeCAD
Complete
3
3D Printing All Parts
Complete
4
Servo Calibration
Complete
5
Standing Pose
Complete
6
Walking Gait
In Progress
7
Turning Gait
Planned
8
Sensor Integration
Planned
9
Autonomous Navigation
Future
55% Complete (5 of 9 Phases)

## Slide 19
Conclusion
Key achievements and future roadmap
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
19/21
Electronics
Systematic debugging validated: I2C chain, servo power rail fix, all 8 servos operational across full 0°–180° range
Mechanical Design
Parametric FreeCAD CAD workflow mastered: , press-fit tolerances, STL export → design-for-manufacture skills
3D Printing
Hands-on material selection (PLA & ABS), slicer optimization, and print quality assessment in CGEC Lab
Overall Platform
Fully functional 8-DOF quadruped hardware + software stack built — validated foundation for walking gait development
Roadmap: Phase 6 Walking Gait (IK) → Phase 7 Turning → Phase 8 Sensors → Phase 9 Autonomous Navigation via ESP32 Wi-Fi

## Slide 20
References
Quadruped Robot Development | Group-E | ECE Dept., CGEC | WTL & MeitY | 2026
20/21
[1]
Previous Batch Project Report — 3D Printing and Embedded Systems, CGEC Dept. of ECE, WTL & MeitY Project, Cooch Behar, West Bengal, 2024
[2]
Espressif Systems, ESP32 Technical Reference Manual, v5.3, Espressif Systems, 2024
[3]
NXP Semiconductors, PCA9685 16-channel 12-bit PWM I2C-bus LED controller, Product datasheet Rev. 4, NXP, 2015
[4]
Tower Pro, SG90S Metal Gear Micro Servo Datasheet, Tower Pro Co. Ltd., 2020
[5]
FreeCAD Community, FreeCAD: Your Own 3D Parametric Modeler, https://www.freecad.org

## Slide 21
THANK YOU
━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━
Quadruped Robot Development | Group-E | CGEC 2026
WTL & MeitY Industrial Training Programme
Guided by: Dr. Palash Das · Mrs. Susmita Banik Barik · Mr. Arijit Bhunia · Mr. Bhaskar Mondal